## Slide 1
美天科技企业
一九九八年十二月
—— CA系列

## Slide 2
Internet
CA系列

## Slide 3
国际互联网的时代
Internet 国际互联网已成为现在及未来不
可或缺的通信工具
使用人数
1997年已达5千万人
2000年可达1亿7千万人（IDG统计）
中国用户在2000年之前可达5百万户

## Slide 4: 迈向Internet移动通信时代
Http://w3.to/skysoft/
WIDE AREA NETWORKS

## Slide 5
Internet通信的里程碑
Internet
ISP
家中
SOHO分公司
SOHO办公室
我们的需要:
越快
越便宜
有效的共用Internet帐号 资源
满足用户的移动办公需要
Argus
路由器
Argus
路由器
Argus
路由器
Argus
路由器
Argus
路由器
Argus完成移动通信的功能
共同连接Internet
远端用户接入存取
办公室间互连
防火墙
外出员工

## Slide 6
H
Internet
支持 ISDN
及56K Modem
中小型办公室(SOHO)需要所有员工共享帐号上Internet
功能 1 -----连接Internet
Argus路由器

## Slide 7
H
Argus路由器
家中或其他地点的办公室
出外人员
SOHO需要可以在家或出外办公
功能 2 -----远端用户可直接进入办公室存取资料

## Slide 8
功能 3 -----办公室间互联
H
H
Internet
SOHO可以ISDN /电话互联，或以Internet上固定IP互联
以固定IP
互联
以电话
或ISDN互联

## Slide 9
功能 4 -----先进的防火墙
H
Argus路由器
出外人员
公司内部人员
家中或其他地点的办公室
1.限制内外部人员能否访问
2.指定那些用户可以或不可以
使用mail / www / FTP / telnet
news，并限制应用的范围
3.NAT
4.代理路由服务器
（防止外部得知内部IP）

## Slide 10
功能 5 -----Internet电子邮件服务器
Internet
Argus路由器
电子邮件服务器
1.一个外部邮件多人共享，并有独立信箱

## Slide 11
功能 5 -----Internet电子邮件服务器
Internet
Argus路由器
电子邮件服务器
1.一个外部邮件多人共享，并有独立信箱

## Slide 12
功能 5 -----Intranet电子邮件服务器
Internet
Argus路由器
电子邮件服务器
1.一个外部邮件多人共享，并有独立信箱
2.内部可用邮件相互通信
3.重要信件可用公告栏通知每个人

## Slide 13
功能 5 -----Intranet电子邮件服务器
Internet
Argus路由器
电子邮件服务器
1.一个外部邮件多人共享，并有独立信箱
2.内部可用邮件相互通信
3.重要信件可用公告栏通知每个人
检查邮件

## Slide 14: 一个地球 一个办公室

## Slide 15
CA产品系列
CA300 Internet Access Server - Internet 傻瓜机
CA320 Internet Access Server - Internet 傻瓜机
CA540 Remote Access Server - 接入服务器
CA545 Remote Access Router - 接入路由器
CA320H Internet Access Server - 集线型傻瓜机
CA320R（CA325）Remote Access Server - 集线
型接入服务器

## Slide 16
CA300
一个RS-232广域接口-接MODEM或
ISDN TA
一个RJ-45以太接口
可同时供多机连接INTERNET

## Slide 17
CA320
一个RS-232广域接口-可以Y型电缆连
接两部MODEM或ISDN TA
一个RJ-45以太接口
可同时供多机连接INTERNET

## Slide 18
CA540
4个RS-232广域接口-可连接4部
MODEM或ISDN TA
一个RJ-45及一个BNC以太接口
可同时供多机连接INTERNET
可同时供远端用户以电话拨人，访问局
域网内部任何一部电脑，如同在本地一样

## Slide 19
CA320H
2个 RS-232 广域接口 - 可以连接两部
MODEM 或 ISDN TA
5个RJ-45以太接口
可同时供多机连接INTERNET

## Slide 20
CA320R－CA325
2个RS－232广域接口－可连接2部MODEM或ISDN TA
5个RJ－45以太接口
可同时供多机连接INTERNET
可同时供远端用户以电话拨入，访问局域网内部任何一部电脑，如同在本地一样

## Slide 21
CA545
4个RS-232广域接口-可连接4部MODEM 或ISDN TA
一个RJ-45及一个BNC以太接口
可同时供多机连接INTERNET
可同时供远端用户以电话拨入，访问局域网 内
部任何一部电脑，并可供用户通过Internet直接
访问局域网内对外公开的16部设备
两个局域网间的路由

## Slide 22
规格
Internet Access
Remote Access
LAN-to-LAN Routing
Firewall
NAT
Filter
Proxy Routing
DHCP
Mail Server
Dial-on-Demand
Bandwidth-on-Demand
Access Authentication
Virtual Server
Network Management
Network Monitor
纯中文版设置

## Slide 23
Mail Server
Windows 3.x
Windows 95 Windows NT
Modem
Internet Access Server
ISP
Internet

## Slide 24
纯中文设置与网管
设置简单：
用户可在一分钟内完成快速设置，超强功能的管理
软件，允许用户进行千变万化的联网解决管理
连接INTERNET：
只要一个帐号，让办公室所有的人都可以上网使用

## Slide 25
远端存取：
允许你从家中或其他办公室，以电话拨入公司内部网，
存取你所需要的资料
办公室间联网：
你不要另买路由器，就可以将各个办公室联网，并开放
部分有合IP地址的服务器供外界访问
保护IP安全：
容许安全的划分对外开放的公网与保密的内部网，并将
开放的IP地址转换成内部私有地址，防止外部人侵或仿
照IP

## Slide 26
限制用户应用权限：
可有效限制用户对HTTP、FTP、SMTP、WWW的使用
电子邮件服务器：
可将任一个EMAIL帐号供多人分享，并保留个人保密信
箱，除可收发INTERNET邮件，也可进行内部邮件收发

## Slide 27
规 格
硬件：80188 CPU 25 MHZ or 40MHZ/10Mbps Ethernet adapter
UART serial port controller/256KB RAM and 256KB flash memory
连接端口：One LAN port RJ-45/One to Four WAN ports D-25
广域网通迅协议：Asynchronous PPP
广域网传输速度：Up to 460Kbps
局域网标准和传输速度：Ethernet 802.3/10BaseT UPT 10Mbps Ethernet
支援前台的工作站：Windows95、Windows NT，Windows3.X,------etc.
支援的通讯协议及保密方式：TCP/IP，NAT，DHCP，PAP/CHAP

## Slide 28
内建功能：Dial-On-Demand,Idle Timer,DHCP Server,IP Address
Mapping,Virtual Server Mapping,Routing,E-Mail
Address Mapping,Remote Access,Access
Control,Bridging
服务器管理软件：Windows-Based configuration/Configuration from
Terminal
电子邮件服务器软件：Mail Server Lite
电源：DC6.0-7.5V,500MA
产品认证：FCC Rules Part 15 Class B, CE Mark
保修年限：1-year warranty

## Slide 29
Can my 2 offices using CA300 to dial up to internet so that the 2 offices can connect to each other using the fix IP Addresses given by ISPs and the others can also surf the internet and their workstations are also protected by firewall?
Ans.Yes.
两部CA机间如何互联？ 简单！

## Slide 30
192.168.1.X Network
Can I connect 2 branch offices’s TCP/IP networks through CA300?
Ans, Yes.
LAN
Routing Table
IP: 192.168.2.0
NetMask: 255.255.255.0
Gateway: 192.168.1.254
Interface: WAN Port1
IP: 0.0.0.0
NetMask: 0.0.0.0
Gateway: 192.168.1.253
Interface: Local Network
Router
192.168.1.253
CA300-1
Server IP:192.168.1.254
Netmask: 255.255.255.0
External Port IP: 1.1.1.1
CA300001.co1
Internet
WAN
Router
192.168.2.X Network
192.168.2.253
CA300-2
LAN
Server IP: 192.168.2.254
Netmask: 255.255.255.0
External Port IP:2.2.2.2
CA300002.co1
Routing Table
IP: 192.168.1.0
NetMask: 255.255.255.0
Gateway: 192.168.2.254
Interface: WAN Port1
IP: 0.0.0.0
NetMask: 0.0.0.0
Gateway: 192.168.2.253
Interface: Local Network

## Slide 31
Can I connect 2 branch offices’s TCP/IP networks through CA320
using ML-PPP?
Ans.Yes.
192.168.1.X.Network
Routing Table
IP 192.168.2.0
Network 255.255.255.0
Gateway 192.168.1.254
Interface WAN Port
LAN
CA320-1
Server IP: 192.168.1.254
NetMask: 255.255.255.0
External Port IP: 1.1.1.1
ML-PPP is enabled
CA320-2
192.168.2.X.Network
Server IP:192.168.2.254
Netmask:255.255.255.0
External Port IP:2.2.2.2
ML-PPP is enabled
Routing Table
IP:192.168.1.0
NetMask:255.255.255.0
Gateway:192.168.2.254
Interface:WAN Port1
WAN
LAN

## Slide 32
Can I connect 3 branch offices’s IP networks through CA320?
Ans.Yes
192.168.1.X Network
LAN
CA320-1
Server IP:192.168.1.254
Netmask:255.255.255.0
External Port 1 IP:1.1.1.1
External Port 2 IP:1.1.1.2
Routing Table
IP: 192.168.2.0
NetMask: 255.255.255.0
Gateway: 192.168.1.254
Interface: WAN Port1
IP: 192.168.3.0
NetMask: 255.255.255.0
Gateway: 192.168.1.254
Interface :WAN Port2
Routing Table
IP: 192.168.1.0
NetMask :255.255.255.0
Gateway: 192.168.3.254
Interface: WAN Port1
IP: 192.168.2.0
NetMask :255.255.255.0
Gateway: 192.168.3.254
Interface: WAN Port2
CA320-2
192.168.X.Network
Routing Table
IP: 192.168.1.0
NetMask: 255.255.255.0
Gateway: 192.168.2.254
Interface: WAN Port1
IP: 192.168.3.0
NetMask: 255.255.255.0
Gateway: 192.168.2.254
Interface: WAN Port2
CA320-2
Server IP:192.168.2.254
Netmask:255.255.255.0
External Port1 IP:2.2.2.1
External Port2 IP:2.2.2.2
Server IP:192.168.3.254
Netmask:255.255.255.0
External Port1 IP:3.3.3.1
External Port2 IP:3.3.3.2
192.168.2.X.Network

## Slide 33
Can I apply for 16 fix IP addresses from ISP and use CA300 as a router?
Ans.Yes
ISP
CA300
168.95.2.1
168.95.2.2
168.95.2.15
Assigned Port IP: 168.95.2.16
Server IP:168.95.2.16
Netmask:255.255.255.0

## Slide 34
Can my 4 fix IP addresses applying from ISP coexistent with
local illegal IP addresses and route through CA300.
Ans.Yes
ISP
CA300
The IP addresses assigned to CA300 are
168.95.2.4
168.95.2.5
168.95.2.6
168.95.2.7
Assigned Port IP:168.95.2.4
Server IP:168.95.2.4
Netmask:255.255.255.0
192.168.2.5
192.168.2.6
192.168.2.7
192.168.2.254
Virtual Server IP Mapping
External IP: 168.95.2.5 External Port: 0
Internal IP: 192.168.2.5 Internal Port: 0
External IP: 168.95.2.6 External Port: 0
Internal IP: 192.168.2.6 Internal Port: 0
External IP: 168.95.2.7 External Port: 0
Internal IP: 192.168.2.7 Internal Port: 0
External IP: 168.95.2.8 External Port: 0
Internal IP: 192.168.2.8 Internal Port: 0

## Slide 35
Can I dial-in to CA540/CA545 to access my company’s TCP/IP or IPX/SPX
network and access the internet through Internet Access Port of CA540/CA545?
Ans.Yes
172.16.1.X Network
Server IP: 172.16.1.254
Netmask: 255.255.255.0
CA545
Port 4
Function: Internet Access Router
Assigned Port IP:168.95.1.19
Internet
Port 4
Port 1
Function:Remote Access
Protocol:TCP/IP and IPX/SPX
Authentication:PAP
User’s William’s IP:172.16.1.100
Win 95(William)
Port 1
Assgned IP:172.16.1.100

## Slide 36
Can I dial-in to CA540/CA545 to access my company’s TCP/IP
network and access another department’s TCP/IP network through another router?
Ans.Yes
172.16.1.X Network
LAN
CA545
Server IP:172.16.1.254
Netmask:255.255.255.0
Port 1
Function:Remote Access
Protocol:TCP/IP and IPX/SPX
Authentication:PAP
User’s William’s IP:172.16.1.100
Win 95 (William)
Port 1
Routing Table:
IP: 172.16.2.0
Netmask: 255.255.255.0
Gateway: 172.16.1.1
Assigned IP:172.16.1.100
Router
172.16.2.X Network
172.16.1.1
172.16.2.1

## Slide 37
Can I dial-in to CA540/CA545 to access my company’s TCP/IP network and surf
the internet through another router?
Ans.Yes
172.16.1.X Network
CA545
Server IP:172.16.1.254
Netmask:255.255.255.0
Port 1
Function:Remote Access
Protocol:TCP/IP and IPX/SPX
Authentication:PAP
User’s William’s IP:172.16.1.100
LAN
Router
Internet
168.16.2.19
172.16.1.1
Port 1
Win 95 (William)
Routing Table:
IP: 0.0.0.0
Netmask: 0.0.0.0
Gateway: 172.16.1.1
Assigned IP:172.16.1.100

## Slide 38
Can CA300s in 4 branch offices dial-in to CA540/CA545 to form an TCP/IP intranet?
Ans.Yes.
192.168.1.X Network
CA545
CA300-2
CA300-3
Assigned IP:192.168.3.1
Assigned IP:192.168.4.1
192.168.3.X Network
192.168.2.X Network
192.168.4.X Network
192.168.5.X Network
CA300-4
CA300-1
Assigned IP:192.168.2.1
Assigend IP:192.168.5.1
Solution 1
Virtual Server IP Mapping Enabled
CA545001.co4
Server IP:192.168.1.254
Netmask:255.255.255.0
Port1 IP:192.168.2.1
Port2 IP:192.168.3.1
Port3 IP:192.168.4.1
Port4 IP:192.168.5.1
Port Function:Remote Access
Server IP: 192.168.2.254
Netmask: 255.255.255.0
Port Function:Internet Access Router
Server IP: 192.168.3.254
Netmask: 255.255.255.0
Port Function:Internet Access Router
Server IP: 192.168.4.254
Netmask: 255.255.255.0
Port Function:Internet Access Router
Server IP: 192.168.5.254
Netmask: 255.255.255.0
Port Function:Internet Access Router
Port 1
Port 2
Port 3
Port 4

## Slide 39
Can CA300s in 4 branch offices dial-in to CA540/CA545 to form an TCP/IP intranet?
Ans.Yes. Solution 2
192.168.2.X Network
CA545
172.16.3.X Network
172.16.4.X Network
172.16.5.X Network
172.16.6.X Network
CA300-1
CA300-2
CA300-3
CA300-4
Assigned IP:172.16.4.1
Assigned IP:172.16.5.1
Assigned IP:172.16.6.1
Assigned IP:172.16.3.1
Server IP: 192.168.2.254
Netmask: 255.255.255.0
Port1 IP: 192.168.2.1
Port2 IP: 192.168.2.2
Port3 IP: 192.168.2.3
Port4 IP: 192.168.2.4
Internet Access Routing
for each port
Routing Table
IP:172.16.3.0
Netmask:255.255.255.0
Gateway:192.168.2.254
Interface:WAN Port 1
IP:172.16.4.0
Netmask:255.255.255.0
Gateway:192.168.2.254
Interface:WAN Port2
IP:172.16.5.0
Netmask:255.255.255.0
Gateway:192.168.2.254
Interface:WAN Port3
IP:172.16.6.0
Netmask:255.255.255.0
Gateway:192.168.2.254
Interface:WAN Port4
Server IP: 172.16.3.254
Netmask: 255.255.255.0
Function:Internet Access Routing
Routing Table:
IP: 192.168.2.0
Netmask: 255.255.255.0
Gateway: 172.16.3.254
Interface: WAN Port 1
Server IP:172.16.4.254
Netmask:255.255.255.0
Function:Internet Access Routing
Routing Table:
IP: 192.168.2.0
Netmask: 255.255.255.0
Gateway: 172.16.4.254
Interface: WAN Port1
Server IP: 172.16.5.254
Netmask: 255.255.255.0
Function:Internet Access Routing
Routing Table:
IP: 192.168.2.0
Netmask: 255.255.255.0
Gateway: 172.16.4.254
Interface: WAN Port1
Server IP:172.16.6.254
Netmask:255.255.255.0
Function:Internet Access Routing
Routing Table:
IP: 192.168.2.0
Netmask: 255.255.255.0
Gateway: 172.16.4.254
Interface: WAN Port1

## Slide 40
Can my 2 offices using CA300 to dial up to internet so that the 2 offfices can connect
to each other using the fix IP Addresses given by ISPs and the others can also
surf the internet and their workstations are also protected by firewall?
Ans.Yes.
ISP
CA300-1
CA300-2
192.168.2.5
192.168.2.6
192.168.2.7
192.168.2.8
192.168.3.9
192.168.3.10
192.168.3.11
192.168.3.12
192.168.2.254
192.168.3.254
ISP Fix IP for CA300-1:
168.95.2.4
168.92.2.5 map to 192.168.2.5
168.95.2.6 map to 192.168.2.6
168.95.2.7 map to 192.168.2.7
Server IP:192.168.2.254
Netmask:255.255.255.0
ISP Fix IP for CA300-2:
168.95.2.8
168.95.2.9 map to 192.168.3.9
168.95.2.10 map to 192.168.3.10
168.95.2.11 map to 192.168.3.11
Assigned Port IP:168.95.2.4
Assigned Port IP:168.95.2.8
Server IP:192.168.3.254
Netmask:255.255.255.0
Notes: <number>
<footer>
<header>
<date/time>